## Slide 1: Introduction to Software Business Product Management
Week 2 Day 3
Led by: Emily Crose
for
Oakland University

## Slide 2: Day 2 Recap

## Slide 3: Questions From Day 2?

## Slide 4: Terms To Listen For
Application Programming Interface (API)
  Enables automated, programmatic retrieval of information using a standard framework.
Authentication
  Refers to the process of verifying a user’s identity.
Rate-Limit
  How many requests can occur at a given time.
Denial of Service
  A forced outage of a service based on a misconfiguration or a concerted effort

## Slide 5: Purdue Model Explained

## Slide 6: Purdue Model, What Is It?
A method of arranging and segmenting networked operational technology (OT) devices.

## Slide 9: Anatomy Of A Complex OT Attack

## Slide 11: Inside The Victim Network

## Slide 12: 10 minute break

## Slide 13: How Does Software Fit In?

## Slide 14: Can This Apply To Cars?
Notes: Can this same concept apply to cars? Of course it can!

## Slide 15: Software By Lines Of Code
Notes: But when we apply the concept of separation of duties to cars, we have to understand what we’re dealing with. By lines of code, modern cars are among the most complexly coded devices around.

## Slide 16: Controller Area Network
Notes: CAN bus devices operate in an interconnected fashion, very similar to how we build computer networks. Controller devices produce information, and we transfer that information over a local area network that we call the CAN or Controller Area Network. That information is packaged in a way similar to the way we package network packets – we saw this last week.

## Slide 17
Notes: This should look at least somewhat similar. The amount of information we’re talking about here is considerably less in CANbus traffic than it is in network packets. It has to be lean because we’re talking about controls that literally make the car move in real time. What you’ll notice about this frame is that there’s nothing here that provides any degree of security.

## Slide 18: SocketCAN
Notes: CAN = Controller Area Network
On the right is the CAN, on the left is socketCAN, a newer implementation of the CANbus

## Slide 19: Where’s the Security??
Notes: There’s very little security on the CANbus, but what security does exist is built into session establishment. The thinking is that we don’t necessarily need to build in security because historically, we could access the CANbus directly, and exclusively through an ODB-II reader. But now we have cars being added to wide area networks through a network connection, so there are more ways of accessing cars now.

## Slide 20: Vehicle Secure Boot
Notes: In this image we have two main parts of the boot microcontroller, the Hardware Security Model (HSM) and the host core. The role of the HSM is to run through the entirety of the system’s memory before allowing the system to boot. The first thing the HSM does is scans a small part of the system’s memory called the host boot manager. Only when all of the integrity checks pass will the HSM allow the vehicle to boot.

## Slide 21: Additional Protocols In Use
ISO-TP
A.K.A. ISO 15765-2
CANopen
GMLAN

## Slide 22: Vehicle Media Systems
Notes: Vehicle media systems are a part of an interconnection of media devices we call MOST. MOST stands for Media Oriented Systems Transport.

## Slide 23: Car Software Attack Surface

## Slide 24: Popular Car Attack Surfaces

## Slide 25: V-Model for Car Engineering

## Slide 26: Risk Based Coding For Cars

## Slide 27: Categorize By Risk
Notes: What we want to do here is separate our entire codebase by the amount of risk it presents.

## Slide 28: References
The Car Hackers Handbook: A Guide For The Penetration Tester by Craig Smith

## Slide 29: Question or clarifications?

## Slide 30: Review Day 3

## Slide 31: Preview Week 3